## Slide 1: Institut Supérieur de l’Aéronautique et de l’Espace Soutenance de Projet de Fin d’Etudes Calibration and Fusion of Stereoscopic and Time-of-Flight Cameras for Zero Gravity Targets Inspection
Auteur: Gabriel Urbain - 3A Supaero - ISAE – France
Encadrants: Daniel Alazard - DEMIA - ISAE – France
José Radzik – DEOS – ISAE - France
Alvar Saenz-Otero – SSL – MIT – USA
Vendredi 24 Octobre 2014

## Slide 2: Overview
Gabriel Urbain – PFE Defense - October 24 2014 2
Introduction
Sensors Features and Acquisition
  Time-of-Flight Camera (Optical Range Finder)
  Stereoscopic Cameras (VERTIGO)
  Thermocam
Calibration Algorithm
  ORF calibration
  Stereo calibration
  System calibration
Fusion Algorithm
Conclusions and Perspectives

## Slide 3: Introduction
Gabriel Urbain – PFE Defense - October 24 2014 3
INSPECT is an extension of SPHERES intending to test pieces of hardware inside the ISS prior to moving into the vacuum of space

## Slide 4: Introductiontion
Gabriel Urbain – PFE Defense - October 24 2014 4
INSPECT adds two cameras to VERTIGO: a thermocam and an Optical Range Finder to perform Visual Navigation.
Thermocam
Optical Range Finder or
Time-of-Flight Camera
Stereoscopic Cameras of
the VERTIGO Goggles

## Slide 5: Introduction
Gabriel Urbain – PFE Defense - October 24 2014 5
Computer Vision enables Simultaneous Localization and Mapping.

## Slide 6: Overview
Gabriel Urbain – PFE Defense - October 24 2014 6
Introduction
Sensors Features and Acquisition
  Time-of-Flight Camera (Optical Range Finder)
  Stereoscopic Cameras (VERTIGO)
  Thermocam
Calibration Algorithm
  ORF calibration
  Stereo calibration
  System calibration
Fusion Algorithm
Conclusions and Perspectives

## Slide 7: Sensors Features and Acquisition
VERTIGO goggles:
Gabriel Urbain – PFE Defense - October 24 2014 7
Feature Detection and matching
uEye API
Triangulation
Stereo Cameras
Optional: Aggregation and Optimization
Feature | Value
Frequency Domain | dominant (visible)
Resolution | 752x480 pixels
Pixel Size | 
FoV | 35°x35°
Output Data | 10 bits monochrome
Feature | Value
Frequency Domain | 
Resolution | 752x480 pixels
Pixel Size | 
FoV | 35°x35°
Output Data | 10 bits monochrome
Two images are captured synchronously

## Slide 8: Sensors Features and Acquisition
Gabriel Urbain – PFE Defense - October 24 2014 8
VERTIGO goggles:
Stereo Cameras
uEye API
Feature Detection and matching
Optional: Aggregation and Optimization
Triangulation

## Slide 9: Sensors Features and Acquisition
Gabriel Urbain – PFE Defense - October 24 2014 9
VERTIGO goggles:
Stereo Cameras
uEye API
Feature Detection and matching
Optional: Aggregation and Optimization
Triangulation
Low-textured objects lead to bad stereo 3D estimations

## Slide 10: Sensors Features and Acquisition
VERTIGO goggles:
Gabriel Urbain – PFE Defense - October 24 2014 10
Stereo Cameras
uEye API
Feature Detection and matching
Optional: Aggregation and Optimization
Triangulation
3D Reconstruction implies knowledge
of intrinsic and extrinsic matrices

## Slide 11: Sensors Features and Acquisition
Gabriel Urbain – PFE Defense - October 24 2014 11
ORF:
ORF Camera
3D Reconstruction
MESA-Imaging API
Feature | Value
Frequency Domain | (far IR)
Resolution | 176x144 pixels
Pixel Size | 
FoV | 69°x55°
Output Data | 14 bits depth, 16 bits visual, 16 bits confidence
Feature | Value
Frequency Domain | 
Resolution | 176x144 pixels
Pixel Size | 
FoV | 69°x55°
Output Data | 14 bits depth, 16 bits visual, 16 bits confidence
Three images are captures in the same time: depth, visual, confidence

## Slide 12: Sensors Features and Acquisition
Gabriel Urbain – PFE Defense - October 24 2014 12
ORF:
ORF Camera
3D Reconstruction
MESA-Imaging API
Three images are captures in the same time: depth, visual, confidence

## Slide 13: Sensors Features and Acquisition
ORF:
Gabriel Urbain – PFE Defense - October 24 2014 13
ORF Camera
3D Reconstruction
MESA-Imaging API

## Slide 14: Sensors Features and Acquisition
Gabriel Urbain – PFE Defense - October 24 2014 14
ORF:
ORF Camera
3D Reconstruction
MESA-Imaging API
ORF is motion sensitive
ORF is material sensitive

## Slide 15: Sensors Features and Acquisition
ORF:
Gabriel Urbain – PFE Defense - October 24 2014 15
ORF Camera
3D Reconstruction
MESA-Imaging API
ORF is exposure sensitive
ORF is range sensitive

## Slide 16: Sensors Features and Acquisition
Gabriel Urbain – PFE Defense - October 24 2014 16
Thermocam:
Feature | Value
Frequency Domain | (near IR)
Resolution | 80x64 pixels
Pixel Size | 
FoV | 44°x36°
Output Data | 8 bits monochrome
Feature | Value
Frequency Domain | 
Resolution | 80x64 pixels
Pixel Size | 
FoV | 44°x36°
Output Data | 8 bits monochrome
The thermocam provides data diversity but with a low resolution

## Slide 17: Overview
Gabriel Urbain – PFE Defense - October 24 2014 17
Introduction
Sensors Features and Acquisition
  Time-of-Flight Camera (Optical Range Finder)
  Stereoscopic Cameras (VERTIGO)
  Thermocam
Calibration Algorithm
  ORF calibration
  Stereo calibration
  System calibration
Fusion Algorithm
Conclusions and Perspectives

## Slide 18: Calibration Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 18
ORF Calibration (intrinsic):
To compute extrinsic parameters, m checkerboard corners are projected and an iterative minimization process is performed:
Intrinsic parameters correspond to intrinsic matrix:
and distortion coefficients :

## Slide 19: Calibration Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 19
VERTIGO Calibration (intrinsic + extrinsic):
Extrinsic parameters corespond to the transformation matrix:
To compute stereo parameters (intrinsic + extrinsic), m checkerboard corners are projected and an iterative minimization process is performed:

## Slide 20: Calibration Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 20
HALO Calibration (extrinsic):
ORF capture
Checkerboard Corners Detection
ORF Pinhole Inversion
Stereo capture
Checkerboard Corners Detection
Stereo Triangulation
Horn’s minimization algorithm in a RANSAC process
Three sets of points are deduced:

## Slide 21: Calibration Algorithm
HALO Calibration (extrinsic):
Gabriel Urbain – PFE Defense - October 24 2014 21
ORF capture
Checkerboard Corners Detection
ORF Pinhole Inversion
Stereo capture
Checkerboard Corners Detection
Stereo Triangulation
Horn’s minimization algorithm in a RANSAC process
From and , we compute 3D points :

## Slide 22: Calibration Algorithm
HALO Calibration (extrinsic):
Gabriel Urbain – PFE Defense - October 24 2014 22
ORF capture
Checkerboard Corners Detection
ORF Pinhole Inversion
Stereo capture
Checkerboard Corners Detection
Stereo Triangulation
Horn’s minimization algorithm in a RANSAC process
From and , we compute 3D points :

## Slide 23: Calibration Algorithm
HALO Calibration (extrinsic):
Gabriel Urbain – PFE Defense - October 24 2014 23
ORF capture
Checkerboard Corners Detection
ORF Pinhole Inversion
Stereo capture
Checkerboard Corners Detection
Stereo Triangulation
Horn’s minimization algorithm in a RANSAC process
The minimization process is:

## Slide 24: Calibration Algorithm
HALO Calibration (extrinsic):
Gabriel Urbain – PFE Defense - October 24 2014 24
ORF capture
Checkerboard Corners Detection
ORF Pinhole Inversion
Stereo capture
Checkerboard Corners Detection
Stereo Triangulation
Horn’s minimization algorithm in a RANSAC process
The minimization process is:

## Slide 25: Calibration Algorithm
HALO Calibration (extrinsic):
Gabriel Urbain – PFE Defense - October 24 2014 25
ORF capture
Checkerboard Corners Detection
ORF Pinhole Inversion
Stereo capture
Checkerboard Corners Detection
Stereo Triangulation
Horn’s minimization algorithm in a RANSAC process
The minimization process is:
Translation axis | CAD Model | Calib with RANSAC | Calib without RANSAC
X |  |  | 
Y |  |  | 
Z |  |  | 
Translation axis | CAD Model | Calib with RANSAC | Calib without RANSAC
X |  |  | 
Y |  |  | 
Z |  |  | 

## Slide 26: Overview
Gabriel Urbain – PFE Defense - October 24 2014 26
Introduction
Sensors Features and Acquisition
  Time-of-Flight Camera (Optical Range Finder)
  Stereoscopic Cameras (VERTIGO)
  Thermocam
Calibration Algorithm
  ORF calibration
  Stereo calibration
  System calibration
Fusion Algorithm
Conclusions and Perspectives

## Slide 27: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 27
Goals of multi-sensor data fusion:
For this algorithm:
Increase accuracy
Increase certainty
Increase completeness
Increase representation

## Slide 28: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 28
Goals of multi-sensor data fusion:
For a future algorithm:
Increase accuracy
Increase certainty
Increase completeness
Increase representation

## Slide 29: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 29
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization
ORF Depth
ORF Visual
ORF Confidence
Stereo Left
Stereo Right

## Slide 30: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 30
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization

## Slide 31: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 31
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization
For each 3D point constructed by the ORF, ORF noise can be reduce to a Normal with variance including:
Thermal noise with variance
Scattering noise with variance

## Slide 32: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 32
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization
The interval can be split in m steps of size

## Slide 33: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 33
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization

## Slide 34: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 34
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization
Each is projected in left and right images and a degree of likeliness is computed around each points:

## Slide 35: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 35
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization

## Slide 36: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 36
Acquisition
Determination of Points Framed by all Sensors
ORF Noise Model
Noise Interval Discretization
Stereo projection
Probability maximization
Probability is computed as:
Where:
And finally,

## Slide 37: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 37
In the first results with INSPECT, fusion (right) does not improve accuracy of the ORF cloud (left)

## Slide 38: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 38
In the first results with INSPECT, fusion (right) does not improve accuracy of the ORF cloud (left)

## Slide 39: Fusion Algorithm
Gabriel Urbain – PFE Defense - October 24 2014 39
Errors seem to come essentially from stereo calibration matrices accuracy and non-linearity of the process

## Slide 40: Overview
Gabriel Urbain – PFE Defense - October 24 2014 40
Introduction
Sensors Features and Acquisition
  Time-of-Flight Camera (Optical Range Finder)
  Stereoscopic Cameras (VERTIGO)
  Thermocam
Calibration Algorithm
  ORF calibration
  Stereo calibration
  System calibration
Fusion Algorithm
Conclusions and Perspectives

## Slide 41: Conclusions and Future Perspectives
Gabriel Urbain – PFE Defense - October 24 2014 41
Acquisition seems to give acceptable results on the ground and during RGA flights.
The calibration algorithm gives good results but could be improved by:
  Adding the thermocam by using a cold/hot checkerboard pattern
  Using better stereo calibration parameters during system calibration
The fusion algorithm does not increase accuracy for the moment (on the ground and during RGA flights) and will not for sure increase completeness and certainty:
  A way to improve it would be a better ORF noise computation or stereo likeliness determination
  The thermocam should be added to create a second point cloud
  Other algorithms have been found that are more adapted to SLAM, avoid the stereo re-projection and consider full objects instead of separated points